## Slide 1: Quad Rat Vitals Monitor
Team:
Jack Ho
Nathan Werbeckes
Joseph Yuen
Guest Starring:
Kuya Takami
Client: Dr. Alex Converse
Advisor: Dr. Tom Yen

## Slide 2: Problem Statement
Vitals for anesthetized rats during PET imaging
  Heart rate (200-500 bpm)
  Rectal temperature (93 – 100° F)
  Respiration rate (20-30 bpm)
Current oximeter is designed for “small animals”
  Inaccurate at faster heart rates
Current devices too expensive
  Budget = $4,000 USD
Problem Statement : Background Info : Design : Future Work
Jack Ho
Team Leader

## Slide 3
Quad Adjustable Isoflurane Delivery*
O2
Isoflurane
Rat
Rat
Rat
Rat
*Slide by Dr. Alex Converse
Problem Statement : Background Info : Design : Future Work
Jack Ho
Team Leader

## Slide 5: Current Devices
Veterinary Oximeters
  Nonin, Bionet, etc.
Starr Life Sciences
  MouseOx
Expensive
Problem Statement : Background Info : Design : Future Work
Jack Ho
Team Leader

## Slide 6: Last Semester’s Final Design
Decided to buy sensors (FSR, pulse-ox, thermistor)
Design and build circuit elements
Integrate and display with LabVIEW
Problem Statement : Background Info : Design : Future Work
Nate Werbeckes
Communicator

## Slide 7: Final Design
Problem Statement : Background Info : Design : Future Work
Computer
LabView
DAq Box
Heart Rate
Blood Oxygen Level
Temperature
Respiratory Rate
Nate Werbeckes
Communicator

## Slide 8: Heart Rate
Pulse-Ox clip
Transimpedance, differential, & non-inverting amp
Process with peak detection algorithm
Display in LabVIEW
Working on: peak detection accuracy
DESIGN : Heart Rate : Temperature : Breathing Rate
Nate Werbeckes
Communicator

## Slide 9: Temperature
Oral Thermometer from Walgreen's
Voltage divider & non-inverting amp
Heat-shrinking plastic
Display and integrate in LabVIEW
It works!
DESIGN : Heart Rate : Temperature : Breathing Rate
Joseph Yuen
BSAC & BWIG

## Slide 10: Breathing Rate
Force Sensing Resistor (FSR)
Voltage divider
Place underneath rat
Display and integrate with LabVIEW
Needs to be tested
DESIGN : Heart Rate : Temperature : Breathing Rate
Joseph Yuen
BSAC & BWIG

## Slide 11: Future Work
Test FSR breathing rate monitor with rat
Choose most accurate peak detection algorithm
Integrate and display all information in LabVIEW
Create full scale model for four rats simultaneously
Problem Statement : Background Info : Design : Future Work
Joseph Yuen
BSAC & BWIG

## Slide 12: References
Webster, J. G., Design of Pulse Oximeters. IOP Publishing Ltd 1997.
Ford D., D. Nachreiner, R. Thomas, “Design of a Pulse Oximeter for Use in Mice”. 2005.
Starr Life Sciences (website). MouseOx
http://starrlifesciences.com/. 2008.
References : Questions

## Slide 13: ?
References : Questions