## Slide 1: Quad Rat Vitals Monitor
Advisor: Peter Klomberg
Client: Alex Converse, Ph.D.

## Slide 2: Overview
PET Imaging
Requirements
Existing Devices
Previous Semester’s Work
This Semester’s Work
Communication Options
Housing Design Options
Where do we go from here?
Acknowledgements

## Slide 3: PET Imaging of Rats
Positron emission tomography (PET) scans to monitor location of radiotracers in rats’ brains
Client scans four anesthetized rats at a time
  Needs to monitor the rats’ vitals
PET scanner at Harlow Primate Lab
Current pulse oximeter used by client

## Slide 4: Device Requirements
Client needs to simultaneously monitor four rats
  SpO2 levels, accuracy of ±2%
  Heart rates up to 500 beats per minute
  Respiratory rates of 20 to 30 breaths per minute
  Rectal temperatures of 93 - 100° F
Non-invasive probes and user-friendly interface

## Slide 5: Existing Devices
Client currently uses rudimentary devices to monitor vitals
Available: MouseOx
  Pulse oximeter for mice and rats
  Over $7000, one rat at a time

## Slide 6: Previous Semester’s Work
Finalized sensors and algorithms to measure temperature and breathing rate
Built pulse oximeter probe
Developed graphical user interface for project
LabVIEW Graphical User Interface
FSR
Pulse Oximeter Probe
Thermistor Probe

## Slide 7: This Semester’s Work
Started developing pulse oximeter calibration curve
Configured LabVIEW to receive data from pulse oximeter
Started integrating thermistor and FSR circuits with ADC of pulse oximeter
Investigated using ‘GumStix’ for data processing

## Slide 8: Communication

## Slide 9: Universal Serial Bus (USB)
Pros:
  Fast communication speed
  Plug and play
  Familiarity
  Inexpensive
Cons:
  Complex programming
  Difficult interfacing with microcontroller
  4 cables would be cumbersome
http://www.novopc.com/wp-content/uploads/2008/10/usb.jpg

## Slide 10: Wireless Fidelity (WiFi™)
Pros:
  Communication speed in excess of device requirements
  Wireless
  Familiarity
  Portability
Cons:
  Expensive
  Susceptible to interference
http://www.freewarepocketpc.net/software_images/wifi-toggler.1.gif

## Slide 11: Bluetooth®
Pros:
  Moderate communication speed
  Easiest to interface with circuit hardware
  Less expensive option
Cons:
  Insufficient number of input ports
  Hard to initially pair with computer
  Computer is not currently Bluetooth compatible
  Requires extensive research
http://www.finesttech.com/wp-content
/uploads/2009/04/bluetooth_large.jpg

## Slide 12
Design Matrix – Communications Link |  |  | 
Criteria | USB | WiFi™ | Bluetooth®
Programming Feasibility (35) | 29 | 28 | 31
Cost( 15) | 12 | 9 | 9
Operability (15) | 12 | 10 | 8
Communication Speed (30) | 25 | 30 | 20
Aesthetics (5) | 1 | 5 | 5
Total (100) | 79 | 82 | 73

## Slide 13: Block Diagram
‘Motherboard’
(GumStix®)
Signal Processing
Rat 1
Board
Rat 2
Board
Rat 3
Board
Rat 4
Board
http://www.computercoupons.com.au/blog/wp-content/uploads/2009/11/lenovo-laptop-computer.jpg

## Slide 14: Circuit Board Housing

## Slide 15: Pegged 3 x 3 Design
Pros:
  Easy to construct
  Simplified installation
Cons:
  Modification of circuit boards is difficult
  Least stable
Receptacles for probes
Pegs for circuit boards

## Slide 16: Toaster Oven Design
Pros:
  Permanent receptacle wall
  Easy access to boards
  Most stable
Cons:
  Precise alignment of receptacles and board required
Grooves for circuit boards
Hinged door

## Slide 17: Bunk Bed Design
Pros:
  Easy access for troubleshooting
  Aesthetically pleasing
  Easy to manufacture
Cons:
  Exposed circuit elements
  Difficult to interface separate boards
Platform for circuit board

## Slide 18
Design Matrix - Housing |  |  | 
Criteria | Pegged 3 x 3 | Toaster Oven | Bunk Bed
Manufacturing Feasibility (30) | 26 | 22 | 26
Ergonomics (40) | 30 | 35 | 25
Durability (20) | 15 | 17 | 14
Aesthetics (10) | 7 | 7 | 10
Total (100) | 78 | 81 | 75

## Slide 20: Where do we go from here?
Construct extra probes
Order materials and build box
Print and build circuit boards
Develop algorithms to process pulse oximeter signal
Finish GUI to incorporate pulse oximeter data

## Slide 21: Acknowledgements
Peter Klomberg
Dr. Alex Converse
Liz Ahlers
Amit Nimunkar
Professor John G. Webster

## Slide 22: Questions?