Product Design Specifications

Rat Quad Vitals Monitor

10/5/08

Team:

Jack Ho		Team Leader 		jyho@wisc.edu

Kuya Takami		Communicator		takami@wisc.edu

Joseph Yuen		BSAC			jyuen@wisc.edu

Nathan Werbeckes	BWIG			werbeckes@wisc.edu

Function:   A monitoring device that will record and display the SpO2 levels and heart rate of four rats simultaneously during PET imaging experiments in order to maintain appropriate anesthesia dosages on each of the four rats independently.  Additionally, it may be able to record and display rectal temperature and breathing rate.

Client requirements: Accurately record and display SpO2 levels and heart rate of four rats under anesthesia simultaneously.

Design requirements: Build a device that takes and displays the vital readings of four rats under anesthesia.  The device must be able to accurately detect heart rates of 200-300 bpm and blood oxygen saturations level accuracy of (2% so that the anesthesiologist is able to determine the adequate dosage of isoflourine to keep the rats anesthetized. If the heart rate and SpO2 levels are accurately detected, respiratory rate (around 20 breaths/min) and rectal temperature (93-100( F) will also be designed into the device.

- Physical and Operational Characteristics

  - Performance requirements: The device, at minimum, should be able to take the SpO2 levels and heart rates of four rats simultaneously and display them onscreen.  It should also have a running graph showing the levels/rates of each rat for the last five minutes.

  - Safety: The device should be safe for animal use and be consistent with the safety standards of the current device.

  - Accuracy and Reliability: The device must be able to accurately detect heart rates of 200-300 bpm and blood oxygen saturations level accuracy of (2%.

  - Life in Service: N/A

  - Shelf Life: N/A

  - Operating Environment: Will be used in a laboratory environment.

  - Ergonomics: The device should, in the end, comfortably fit onto the hind paw of each rat without affecting the device’s performance or accuracy.

  - Size: Clips must be small enough so that it will not interfere with surrounding sensor and/or devices. Standard small animal oximeter sensor.

  - Weight: Standard small animal sensor.

  - Materials: We will be using already commercially available oximeter sensors.  All other materials will not be in contact with the rats.

  - Aesthetics, Appearance, and Finish: N/A

- Production Characteristics

  - Quantity: One.

  - Target Product Cost: under $4,000

- Miscellaneous

  - Standards and specifications:N/A

  - Customer: Research organizations working with rats.

  - Patient-related concerns: Currently no patient-related concerns.

  - Competition: MouseOx