## Slide 1: Cartilage bioreactor
Sarah Springborn
Luisa Meyer
BeomKang Huh
Sarah Czaplewski
Client: Dr. Wan Ju Li
Advisor: Professor Block

## Slide 2: Overview
Joint Trauma and Degeneration
  Current Treatments
  Future Directions
Non-Destructive Testing for Tissue Engineering
  Requirements for High Field MR
MR Compatible Bioreactor Designs
Assessment of Materials and Deformation Methods
Bioreactor Construction and Validation

## Slide 3: Cartilage Damage and Treatments
Cartilage cannot repair itself
Accident/Injury
Osteoarthritis
  Cartilage between joints wears away
  Affects 21 million Americans
Current Treatments
  Cartilage transfer
  Joint replacement

## Slide 4: Cartilage Regeneration
Goal: repair lesions to articular cartilage
Stem cells removed from patient
Cells grow in scaffold
Cells mature and differentiate due to applied conditions
Mature cells are implanted to fill lesions

## Slide 5: Non-Destructive Testing
Current Methods
  Testing throughout stages of development
  Destroys cells
  Isolates proteins, genes, etc for analysis
Proposed Method
  Testing throughout stages of development
  Cells remain viable
  Images of mechanical loading

## Slide 6: Requirements for MR and Compression
Material
  Biocompatible
  Autoclave and MR safe
Physical Design
  3 inch diameter
  Leak-proof removable cap
Mechanical Loading
  Tissue cannot move
  5-20% Deformation
~3 mm
~1.5 cm

## Slide 7: Plunger Compression
Side View of Bioreactor
Manual twist or push compression
Removable fixation
Cap
Guide rails for fixation to slide into
Compressor
Tissue
Legs to lift tissue off the bottom
Side View of Fixation
Rubber Seal

## Slide 8: Lever Compression

## Slide 9: Angled Compression

## Slide 10: Design Matrix - Materials
 | Resistance to Heat* | Transparency* | Durability | Cost | Ease of Fabrication | Total (35)
Bioceramics | 10 | 2 | 1 | 1 | 1 | 15
Teflon | 10 | 2 | 5 | 2 | 2 | 21
PVC | 4 | 10 | 4 | 3 | 5 | 26
Poly-carbonate | 6 | 10 | 4 | 5 | 5 | 30
* The score is weighted by a factor of two

## Slide 11: Design Matrix – Overall Designs
 | Risk of Leakage* | Fixation* | Maintain Force* | Durability | Ease of Fabrication | Cost | Total (50)
Plunger | 8 | 6 | 8 | 4 | 5 | 3 | 38
Lever | 6 | 8 | 4 | 3 | 2 | 1 | 28
Angled | 6 | 8 | 6 | 4 | 4 | 3 | 35
* The score is weighted by a factor of two

## Slide 12: Proposed Design
Manual twist or push compression
Removable fixation
Cap
Guide rails for fixation to slide into
Compressor
Tissue
Legs to lift tissue off the bottom
Side View of Fixation
Side View of Bioreactor
Rubber Seal
Clear Polycarbonate Plastic

## Slide 13: Bioreactor Validation
Create “mock-up” of design
Determine thermal conductivity of imaging coil
Observe temperature decay
Establish necessary volume of medium for imaging
  Air space

## Slide 14: Bioreactor Construction
Order components
  Polycarbonate
  Non-ferrous hardware
Fabricate prototype

## Slide 15: References
Articular Cartilage Restoration." 01 Feb 2009. American Academy of Orthopaedic Surgeons, Web. 11 Oct 2009. <http://orthoinfo.aaos.org/topic.cfm?topic=A00422>.
"Osteoarthritis." MedicineNet. Web. 11 Oct 2009. <http://www.medicinenet.com/osteoarthritis/article.htm>.
Tuli, Richard, Wan-Ju Li, and Rocky Tuan. "Current State of Cartilage Tissue Engineering." Arthritis Research & Therapy 5.5 (2003): n. pag. Web. 11 Oct 2009. <http://www.pubmedcentral.nih.gov/articlerender.fcgi?artid=193737>.

## Slide 16: Acknowledgments
Thank you to:
  Dr. Li
  Professor Block

## Slide 17: Questions?